## Slide 1: Thermostat system
Vlad Veliciu

## Slide 2: Block diagram

## Slide 3: Types of temperature sensors

## Slide 4: Semiconductor-based IC temperature sensor
No. | Name | Temp range (°C) | Gain (mV/°C) | Supply voltage (V) | Supply current when measuring (µA) | Accuracy (°C) | Price (RON)
1. | TMP236AQDBZRQ1 | -10 +125 | 19.5 | 3.1…5.5 | 14.5 | +/-2.5 | 6.53
2. | MAX6611AUT+T | -40 +125 | 16 | 4.5…5.5 | 150 | +/-1 | 23.51
3. | MAX6605MXK+T | -55 +125 | 11.9 | 2.7…5.5 |  | +/-0.75 | 10.00
4. | TMP235A2DBZR | -40 +150 | 10 | 2.3…5.5 | 15 | +/-0.5 | 6.93
5. | LMT70YFQT | -55 +150 | 5.194 | 2.2…5.5 | 12 | +/-0.2°C | 12.73

## Slide 5: Semiconductor-based IC temperature sensor
LMT70YFQT
an ultra-small, high-precision, low-power CMOS analog temperature sensor

## Slide 6: Types of humidity sensors
1. Capacitive
Thin strip of hygroscopic polymer film as dielectric
The dielectric dependent to the relative humidity

## Slide 7: Types of humidity sensors
2. Resistive
Materials with low resistivity that varies inverse proportional with humidity
Used materials: salt, conductive polymeres

## Slide 8: Types of humidity sensors
3. Thermal conductivity
2 thermistors are used
Measures conductivity of dry air and air with water vapors and the difference = absolute humidity

## Slide 9: Capacitive humidity sensor
No. | Name | Range (% RH) | Supply voltage (V) | Supply current when measuring (µA) | Accuracy (% RH) | Price (RON)
1. | SHT40-AD1B-R3 | 0 100 | 1.08…3.6 | 320 | +/-1.8 | 12.57
2. | DHT11 | 20 90 | 3…5 | 500 | +/-5 | 10.85
3. | SHT31-DIS-B2.5kS | 0 100 | 2.4…5.5 | 600 | +/-2 | 24.21
4. | HS3004 | 0 100 | 3.3…5.5 | 7 | +/-3.5 | 12.23
5. | HS3001 | 0 100 | 3.3…5.5 | 24.4 | +/-1.5 | 32.92

## Slide 10: Capacitive humidity sensor
SHT40-AD1B-R3

## Slide 11: Connecting the analog temperature sensor - Required elements

## Slide 12: Types of ADC
ADC type | How it works? | Conversion time
Flash | n-1 comparators, comparing Vin with levels of Vref | ~propagation time (fast)
ADC implemented with counter | DAC + counter counting only up | (max)
ADC implemented with up/down counter | DAC + counter up/down | every
ADC with Successive Approximation Registers (SAR) | DAC + SAR + needs S/H | 
ADC type | How it works? | Conversion time
Flash | n-1 comparators, comparing Vin with levels of Vref | ~propagation time (fast)
ADC implemented with counter | DAC + counter counting only up | 
ADC implemented with up/down counter | DAC + counter up/down | 
ADC with Successive Approximation Registers (SAR) | DAC + SAR + needs S/H | 

## Slide 13: ADC0808
Characteristics:
Conversion time: 100 µs
Voltage Supply: 4.5V … 6V (typical 5V) (VREF + = 5V and VREF - = 0V)
Total error: +/- 0.5 LSB
Clock frequency: 640 kHz

## Slide 14: ADC0808
START = start of conversion
EOC = end of conversion
OE = output enable

## Slide 15: Amplification needed?
Sensor LM45: gain of 10 mV/°C
At 0°C => Vout=0V and at 50°C => Vout=0,5V
ADC: At 0°C => Out=0h and at 50°C => Out=FFh (255; 255*VLSB=Vin => Vin=4,99V)
Conclusion: Amplification is needed (A=4,99/0,5=9,98)
=> Choose an Operational Amplifier

## Slide 16: AD8603
Characteristics:
Low offset voltage: 50µV
Single-supply operation: 5V
Precision amplifier
High CMRR: 100dB
Rail-to-rail

## Slide 17: Non-inverting amplifier

## Slide 18: Implementing in Proteus

## Slide 19: Implementing in Proteus: case 50°C

## Slide 20: Implementing in Proteus: case 0°C

## Slide 21: How does the LCD work?
2 polarized panel filters and electrodes
Principle of blocking light
Working:
Current applied to liquid crystal molecule
Molecule tends to untwist
Angle of light changes
Angle of polarizing filter changes
-> that area becomes blank

## Slide 22: How does the LCD work?
HD44780U standard communication
Chosen LCD: LM016L (16x2 display)
Signals:
RS: 0 (command), 1 (information)
RW: 0 (write), 1 (read)
EN: low when setting other lines, put in high for a min period of time (230 ns for writing), then in low again
D0…D7: data lines

## Slide 23: Commands for the LCD
Instruction | RS | R/W | D7 |  | D6 |  | D5 |  | D4 |  | D3 |  | D2 |  | D1 |  | D0 | Hex code (D7…D0)
16x2 LCD (init) | 0 | 0 | 0 |  | 0 |  | 1 |  | 1 |  | 1 |  | 0 |  | 0 |  | 0 | 38h
Place cursor | 0 | 0 | 0 |  | 0 |  | 0 |  | 0 |  | 1 |  | 1 |  | 1 |  | 0 | 0Eh
Clear display | 0 | 0 | 0 |  | 0 |  | 0 |  | 0 |  | 0 |  | 0 |  | 0 |  | 1 | 01h
Write a character | 1 | 0 | ASCII code for the character (D0=LSB and D7=MSB) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Move cursor on line 2 | 0 | 0 | 1 | 1 |  | 0 |  | 0 |  | 0 |  | 0 |  | 0 |  | 0 |  | C0h
Move cursor on line 1 | 0 | 0 | 1 | 0 |  | 0 |  | 0 |  | 0 |  | 0 |  | 0 |  | 0 |  | 80h
Cursor off | 0 | 0 | 0 | 0 |  | 0 |  | 0 |  | 1 |  | 1 |  | 0 |  | 0 |  | 0Ch
Display off, cursor off | 0 | 0 | 0 | 0 |  | 0 |  | 0 |  | 1 |  | 0 |  | 0 |  | 0 |  | 8h
After setting the signals for every instruction, the EN signal needs to be put from LOW to HIGH, then after the minimum period again in LOW.

## Slide 24: Writing on the LCD
Instr | RS | R/W | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
Init LCD | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0
Cursor on | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0
V | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
L | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0
A | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
D | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
New line | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
V | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
E | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1
L | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0
I | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1
C | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
I | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1
U | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
Cursor off | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0

## Slide 25: Writing on the LCD

## Slide 26: Choosing the Microcontroller (80C51 family)
Main characteristics (usually):
4kB internal ROM
128B internal RAM
Some signals:
ALE/PROG
PSEN: external program memory read strobe
EA (External Access Enable)/Vpp:
EA low -> external memory code
EA high -> internal memory code

## Slide 27: Microcontrollers from the 80C51 familiy
No. | Name | RAM size | ROM size | Voltage range (V) | Clock frequency (MHz) | I/O ports | ADC intern | Price (RON)
1. | C8051F986-C-GU | 512x8 | 8kx8 | 1.8…3.6 | 25 | 17 | yes | 16.53
2. | AT89LP828-20AU | 768x8 | 8kx8 | 2.4…5.5 | 20 | 30 | no | 15.15
3. | AT89LP51RB2-20JU | 256x8 | 24kx8 | 2.4…5.5 | 20 | 40 | yes | 19.85
4. | AT89LP51-20JU | 256x8 | 4kx8 | 2.4…5.5 | 20 | 36 | no | 17.08
5. | AT89LP51RB2-20AU | 256x8 | 24kx8 | 2.4…5.5 | 20 | 40 | yes | 18.96

## Slide 28: The AT89LP51RB2-20AU microcontroller

## Slide 29: Complete electrical schematic in Proteus

## Slide 30: Crystal oscillator
Between XTAL1 XTAL2, inverting amplifier
Capacitors ensure phase stability + frequency selection from the crystal oscillator

## Slide 31: Buttons
PLUS Button on external interrupt INT0
MINUS on INT1

## Slide 32: Relay
Output ‘1’ from uC => transistor ON => current flow => metallic arch pushed towards the coil with magnetic core
Output ‘0’ => metallic arch pushed away

## Slide 33: Voltage Regulator
Gives at output 5V to supply the electronic devices
Decoupling capacitors for eliminating the noise

## Slide 34: Simulation